## Slide 1
On Becoming a Leader in Risk Management
ENGG404 - Lecture
Glossary
Fundamentals of RM
RM System and Process
Application and Perspectives
People & Org.
Incident Investigation
RM Tools & Challenges
Leadership in RM
RM in Industry

## Slide 2
Generalize the terminology widely used in the field of risk management.
Find the important terms.
Differentiate between terms.
Several key terms will be quickly reviewed:
Refer to Glossary: Definitions of Terms & Phrases
Learning Outcomes:
2
Glossary: Definitions of Terms and Phrases
Notes: 2

## Slide 3
Learning Outcomes:
3
Glossary: Definitions of Terms and Phrases
Engineering Safety and Risk Management | ESRM is the integrated system / program for, or the approach to, the management of the continuous reduction of risk to people, environment, assets, and production / productivity. Within the industrial setting, it may be referred to as Industrial Safety and Risk Management, Industrial Safety and Loss Management, or Process Safety Management.
Notes: 3
The system by which we manage risk to people, the environment, and business
Aka industrial safety and risk management, process safety and risk mgmt

## Slide 4
Learning Outcomes:
4
Glossary: Definitions of Terms and Phrases
Accident | Many people understand the term accident. However, the connotative meaning of accident refers to an undesired event that is “believed” to be beyond the control of people; an undesired event that results in harm to people, damage to property, damage to environment or loss to process - or a combination of all. Thus, accidents are then deemed an inevitable consequence of doing business. Contrast this with the position taken by leading companies and loss prevention specialists: they believe all accidents are preventable. It is arguable that the term accident is not only wrong, but the very use of the term accident is counterproductive to loss management initiatives. See Incident or Event.
Incident or Event; Incident Description | An undesired and specific event, or sequence of events that could result in or has resulted in harm to people, harm or damage to the environment, loss or damage to property or assets, loss to a process or loss of production / productivity — or a combination of all.
Notes: 4
Important distinction!
Accident infers that it was not preventable – wrong!!!
Think about driving down the road and getting into an ‘accident’

## Slide 5
Observation, Conclusion, Recommendation, …
Please confer to draw a conclusion, a recommendation, and an opinion. Note your thoughts to your classmate or yourself.
“Observation, Conclusion, Recommendation, and Opinion”:
When faced with a problem, and a decision must be made:
Observation: You read the thermometer outside … -40⁰C. Your household thermostat indicates it is 6⁰C inside.
Conclusion: ?
Recommendation: ?
Opinions: ?
5
Glossary: Definitions of Terms and Phrases
Notes: 5

## Slide 6
Observation, Conclusion, Recommendation, …
6
Chapter x.x: title
“Observation, Conclusion, Recommendation, and Opinion”:
When faced with a problem, and a decision must be made: Consider a decision about your home heating system.
Observation: You read the thermometer outside … -40⁰C. Your household thermostat indicates it is 6⁰C inside.
Conclusion: What is (are) your conclusion(s)? It is colder outside the house than inside, it less than room temperature in the house.
Recommendation: What is (are) your recommendation(s)? Check to see if the furnace is working. Check to see if a window is open.
Opinions:
Notes: 6
Check to see if the furnace is working
Check to see if a window has a leak

## Slide 7
Any questions?
Notes: 7