## Slide 1
On Becoming a Leader in Risk Management
ENGG404 - Lecture
Chapter 5.2:
The Fundamental Approach to Control All Risks (Hierarchy of Effectiveness)
Fundamentals of RM
RM System and Process
Application and Perspectives
People & Org.
Incident Investigation
RM Tools & Challenges
Leadership in RM
RM in Industry

## Slide 2
Explain two different approaches for a Risk Reduction Hierarchy:
AB OH&S Code Part 2 Hazard Assessment, Elimination, and Control
ANSI Z10-2012: Risk Reduction Hierarchy & Hierarchy of Effectiveness
Apply the two different approaches to identify, evaluate, and select the most effective risk reduction solution(s).
Explain that order of effectiveness is NOT an order of priority.
Learning Outcomes:
2
Chapter 5.2: Fundamental Approach to Control All Risks
Notes: 2
APEGA’ minimum requirements

## Slide 3
You want to implement the most effective risk reduction solutions i.e. the safeguards or control measures in the form of engineering controls & administrative controls.
How do you identify, evaluate, and select the most effective risk reduction solutions i.e. the most effective safeguard / control measure?
The fundamental approach to control all risks is simply a hierarchy.
Two approaches (of many) are:
AB OH&S Code Part 2 Hazard Assessment, Elimination, and Control
ANSI Z10-2012: Risk Reduction Hierarchy & Hierarchy of Effectiveness
Risk Reduction Hierarchy & Hierarchy of Effectiveness
3
Chapter 5.2: Fundamental Approach to Control All Risks
Notes: 3
APEGA’ minimum requirements

## Slide 4
AB OH&S Code Part 2 Hazard Assessment, Elimination, and Control
The AB OH&S Code Part 2 Section 9 specifies the order of effectiveness, a basic approach of a Risk Reduction Hierarchy:
  Eliminate
  Apply Engineering Controls to Reduce the Exposure
  Apply Administrative Controls and Work Practices to Reduce the Exposure
  Use PPE
  Use combinations of above.
Most facilities usually apply and “prioritize” PPE first” because it is easy even though it is the least effective!
AB OH&S Code Part 2:
4
Chapter 5.2: Fundamental Approach to Control All Risks
Notes: 4
APEGA’ minimum requirements

## Slide 5
ALE #1: Apply AB OH&S Code Part 2 to Spray-Patch Crew
Please confer and respond (Open discussion):
Consider this job (activity) and its hazards:
Job: typical spray-patch crew: crack is gouged, sprayed with hot tar-oil, filled and tamped with pea gravel.
Hazards to address: exposure to traffic, crushed by moving dump truck, repetitive shoveling / spraying motions, contact with hot tar.
Choose 1 hazard and apply the AB OH&S Code Part 2.
5
Chapter 5.2: Fundamental Approach to Control All Risks
Eliminate
Apply Engineering Controls to Reduce the Exposure
Apply Administrative Controls and Work Practices to Reduce the Exposure
Use PPE
Use combinations of above.
Notes: 5
APEGA’ minimum requirements

## Slide 6
Example: Apply AB OH&S Code Part 2 to Spray-Patch Crew
6
Chapter 5.2: Fundamental Approach to Control All Risks
Eliminates: crushed by moving dump truck, repetitive shoveling motion,
contact with hot tar.
Eliminates: crushed by moving dump truck, all repetitive motions, contact with hot tar AND exposure to traffic.
Notes: 6
APEGA’ minimum requirements

## Slide 7
ANSI Z10-2012: Risk Reduction Hierarchy & Hierarchy of Effectiveness
7
Chapter 5.2: Fundamental Approach to Control All Risks
ANSI Z10-2012 has same order as AB OH&S but includes “substitution”.
Notes: 7
Order of effectiveness, not priority!!! Maybe you prioritize using PPE in a lab because it’s easy, but not the most effective way of reducing risk.
Apply engineering controls – encompasses substitute, isolate/separate, engineer
Apply admin controls – organization and procedures (there’s a policy for when you wear ppe)
PPE – work practices (I am wearing my ppe)
They work together

## Slide 8
ANSI Z10-2012: Risk Reduction Hierarchy & Hierarchy of Effectiveness
8
Chapter 5.2: Fundamental Approach to Control All Risks
Notes: 8

## Slide 9
Examples of Application of ANSI Z10-21012:
9
Chapter 5.2: Fundamental Approach to Control All Risks
Hierarchy Level | Example
Eliminate | Evacuate the piping system of the hazard. Fill in the hole to eliminate a fall hazard.
Substitute | A non-toxic substance instead of a toxic substance
Isolate / Separate | A work platform instead of using personal fall arrest. Closed-loop sampling system.
Engineering Controls | Noise-dampening technology to reduce noise levels. Mechanical-assist lifting devices instead of physical effort. Exhaust ventilation system to draw away contaminated air e.g. fume hood or welding hood.
Warnings / Organization | Train workers to observe warning signs, labels, alarms, and how to respond Additional workers for relief and rotation in hazardous conditions e.g. hot weather / hot environments.
Administrative Controls | Policies / procedures (PTWs, checklists, JSAs, FLRAs, SQRAs, etc.) that describe how to do the safe execution of work e.g. walk on designated in-plant walkways
PPE | Flame retardant clothing, hard hats, eye protection, respiratory protection, face protection, gloves, safety boots, flash suit
Notes: 9
Potentially tie in Fernie example with regard to engineering controls (substitute, isolate, engineer)
-replace the brine with ethylene glycol (antifreeze) – substitute, or replace the ammonia with freeon - substitute
-use a more corrosion resistant heat exchanger (shellen tube?) -

## Slide 10
ALE #2: Apply ANSI Z10 to Fernie Arena Refrigeration System
Please confer (Open discussion):
How would you apply the ANSI Z10-2012 hierarchy of controls to the refrigeration system hazards at the Fernie Arena? Identify 1 or 2 examples.
10
Chapter 5.2: Fundamental Approach to Control All Risks
Hierarchy Level | Example
Eliminate | 
Substitute | Freon-type refrigerant instead of ammonia
Isolate / Separate | 
Engineering Controls | 
Warnings / Organization | 
Administrative Controls | 
PPE | self-contained breathing air
Notes: 10
Potentially tie in Fernie example with regard to engineering controls (substitute, isolate, engineer)
-replace the brine with ethylene glycol (antifreeze) – substitute, or replace the ammonia with freon - substitute
-use a more corrosion resistant heat exchanger (higher alloys)

## Slide 11
Apply AB OH&S Code Part 2 to Spray-Patch Crew
Apply ANSI Z10 to Fernie Arena Refrigeration System
The intent is to give you an opportunity to practice these approaches, and NOT to instruct you on specific solutions to these problems.
Intent of These Active Learning Exercises:
11
Chapter 5.2: Fundamental Approach to Control All Risks
Notes: 11
APEGA’ minimum requirements

## Slide 12
Key Difference Between Hierarchy of Effectiveness & Order of Priority:
12
Chapter 5.2: Fundamental Approach to Control All Risks
This tool is a hierarchy of effectiveness and yields an order of effectiveness, NOT an order of priority.
In a future seminar, the Complex Effort vs Gain Tool will be presented; this tool helps us to prioritize the implementation of recommendations.
Notes: 12
I.e. PPE – you prioritize it because it’s easy and cheap, but it is not the most effective risk reduction solution!

## Slide 13
Any questions?
Notes: 13