## Slide 1
On Becoming a Leader in Risk Management
ENGG404 - Lecture
Case 4: Lithium ion Battery Fires in Electric Vehicles
Fundamentals of RM
RM System and Process
Application and Perspectives
People & Org.
Incident Investigation
RM Tools & Challenges
Leadership in RM
RM in Industry

## Slide 2
Explain the technical safety aspects of lithium ion battery fires and why they are considered a low frequency, high consequence risk scenario
Describe the bow tie approach for depicting key concepts in risk management
Apply the prevention through design (PTD) concept for the future of electric vehicle batteries
Learning Outcomes
2
Case 4: Lithium Ion Battery Fires in Electric Vehicles
Notes: 2

## Slide 3
Superior attributes of Lithium ion battery
Higher current, voltage, power and energy density
Reduced cost, weight and pollution
Lack of memory effect
Excellent stability
Low self-discharge rate
Prolonged life cycle
Used in a variety of applications
Small cells in consumer electronics
Large scale packs in the electrification of road transport and smart grids
Managing peaks and valleys associated with output from wind and solar
Introduction
3
Case 4: Lithium Ion Battery Fires in Electric Vehicles
Notes: 3

## Slide 4
Cells produce an electric current by converting chemical energy into electrical energy
Two electrodes
  Negative (anode) - typically made of carbon (graphite)
  Positive (cathode) - generally consists of layers of lithium and metal oxide
Permeable barrier between the electrodes prevents internal short-circuiting
Electrolyte transfers charged ions between the electrodes. It consists of a lithium salt dissolved in an organic solvent, mainly carbonates.
Energy is related to the chemistry and construction of the LIB cell
Battery Design
4
Case 4: Lithium Ion Battery Fires in Electric Vehicles
Notes: 4

## Slide 5
Multi-cell Pack for Tesla Model S:
5
Case 4: Lithium Ion Battery Fires in Electric Vehicles
Notes: 5

## Slide 6
Overview
Volatile organic electrolyte solution (hazardous)
Short circuit or high operating temp. can lead to exothermic reactions
Worst case scenario - battery catches fire or explodes (low frequency)
Different fire in terms of initiation, spread, duration, toxicity & suppression
Increase in fire risk is proportional to the increase in the mass and capacity of the battery (the fuel)
Last two decades
Variety of fires (small consumer electronics to large power systems)
Initial concerns with portable devices (cell phones and laptops)
Sony (2006) recalled 9.6 million notebooks with LIBs ($400 million)
Samsung (2016) recalled 2.5 million Note 7 smartphones ($17bn)
Boeing 787 Dreamliner grounding in 2013 (1.1 million USD/day loss)
Variety of electric vehicle fires including Chevy Volt and Tesla Model S
LIB Fires
6
Case 4: Lithium Ion Battery Fires in Electric Vehicles
Notes: 6

## Slide 7
EV battery packs = composed of thousands of single cells
A thermal runaway (TR) can initiate in a single cell and propagates to other cells in the pack
LIB temp. reaches a critical value such that the reaction rate of an exothermic reaction increases the temp. & accelerates the reaction rate
A fast process that occurs at a time scale <2 s, leading in most cases to battery rupture in less <0.01 s
Triggers for LIB TR
  External abuse (mechanical, thermal, electrical)
  Internal failure (defects, self-heating)
  Critical for LIB to balance heat generation with heat dissipation
Thermal Runaway
7
Case 4: Lithium Ion Battery Fires in Electric Vehicles
Notes: 7

## Slide 8
LIB TR & Imbalance Between Heat Generation & Dissipation:
8
Case 4: Lithium Ion Battery Fires in Electric Vehicles
Notes: 8

## Slide 9
Electric Vehicle LIB related Fires
9
a) A Renault-Samsung EV caught fire while driving (January 2016, Korea)
b) A pure battery electric bus caught fire in a charging station (April 2015, Shenzhen, China)
Case 4: Lithium Ion Battery Fires in Electric Vehicles
Notes: 9
9

## Slide 10
Electric Vehicle LIB related Fires
10
c) A Tesla Model S released smokes while being driven (June 2018, California)
d) EV fire in a parking lot (May 2018, Hangzhou, China)
Case 4: Lithium Ion Battery Fires in Electric Vehicles
Notes: 10
10

## Slide 11
Chain of Events after abusing a LIB
11
Case 4: Lithium Ion Battery Fires in Electric Vehicles
Notes: 11

## Slide 12
  Preventing battery failure which sometimes lead to thermal runaway reactions & fires has remained a challenge for LIBs
  Recall PTD focus is to “engineer out the hazards” through our designs
  PTD focus area is battery chemistry and design to prevent TR fires
  PTD with inherently safer materials:
    Cathode chemistry
    Modified separators
    Modified electrolytes
    Solid state batteries
Prevention Through Design
12
Case 4: Lithium Ion Battery Fires in Electric Vehicles
Notes: 12

## Slide 13
Potential PTD Opportunities for LIBs
13
Case 4: Lithium Ion Battery Fires in Electric Vehicles
Notes: 13

## Slide 14
LIB technology is superior but the current designs have the risk of a low frequency, high consequence risk event (fires to thermal runaway)
A variety of LIB-related fires have occurred over the last two decades
A bow tie diagram provides a simple visual depiction of a complex situation (especially when dealing with non-specialists)
Prevention through design opportunities are in the area of inherently safer design that reduce the frequency of LIB-related fires
Summary & Key Lessons
14
Case 4: Lithium Ion Battery Fires in Electric Vehicles
Notes: 14

## Slide 15
Any questions?
Notes: 15