## Slide 1
On Becoming a Leader in Risk Management
ENGG404 - Lecture
Chapter 2.5: What is an Acceptable Level of Risk?
Fundamentals of RM
RM System and Process
Application and Perspectives
People & Org.
Incident Investigation
RM Tools & Challenges
Leadership in RM
RM in Industry

## Slide 2
Interpret a set of risk criteria to determine a risk level.
Construct risk matrices for simple operations and systems, and evaluate the acceptance of risks through these matrices.
Apply a generic risk matrix to decide whether to accept the residual risk and manage it, or determine if additional control measures / safeguards are needed to reduce the risk to an acceptable level.
Learning Outcomes:
2
Chapter 2.5 What is an Acceptable Level of Risk?
Notes: 2

## Slide 3
Acceptable Level of Risk:
3
Chapter 2.5 What is an Acceptable Level of Risk?
TRUE or FALSE?
If climbing a ladder is a high hazard activity, then it is a high risk activity.
False
  Even though climbing a ladder is a high hazard activity, it is not necessarily a high risk activity.
  High hazard potential does not equate to high risk.
Why? You can apply control measures to the high hazard activity in order to reduce the risk to an acceptable level.
How? You can either:
              Reduce the likelihood or
              Reduce the consequence, or
              Reduce both,
              Reduce (control) or eliminate the hazard.
Notes: 3
Just because an activity has significant hazards, does not mean that it is a high risk activity. You can implement measures to reduce risk to an acceptable level.

## Slide 4
Risk is a function of consequence and likelihood.
Thus, safeguards (control measures) can be implemented to:
reduce the consequence, or
reduce the likelihood, or
eliminate, reduce, or control the hazard.
Build on Chapter 2:
4
Chapter 2.4 Risk as a Function of Likelihood and Consequence
Risk
How bad can it be?
How likely is it to occur?
What can go wrong?
Is Risk Acceptable?
Do NOT do (or stop doing)
the activity.
Do (or keep doing)
the activity.
NO
YES
Reduce the consequence
Reduce the likelihood
Reduce (control), or Eliminate the hazard
Notes: 4

## Slide 5
The Simple Risk Matrix:
5
Chapter 2.5 What is an Acceptable Level of Risk?
Terms Used:
Simple = Fundamental
Consequence = Impact =
Severity
Likelihood = Probability = Frequency = Rate
Simple Risk Matrix:
Increasing Consequence
Increasing Likelihood
M | H | H
L | M | H
L | L | M
L M H
H
M
L
Notes: 5
But how do we define L, M, H?

## Slide 6
L, M, H Consequence and L, M, H Likelihood (This is relative and will change depending on the company.)
Risk Criteria Table:
6
Chapter 2.5 What is an Acceptable Level of Risk?
Ratings | Impact on PEAP (Consequences) | Likelihood
High | High P Disabling injury, loss of body part or fatality. E Reportable violation, toxic release. A High repair cost (Typically > $100k). Pr Loss of function of facility for extended period, with business consequences, major quality deviation. | High Repetitive event. At least once per year Several times in the life cycle of a project. Has happened frequently in similar circumstances. Greater than 50% chance of occurring.
Medium | Medium P Medical Aid injury. E Non-reportable spill, non toxic release. A Moderate repair cost (typically > $10k). Pr Short duration loss of function, serious quality deviation, medium business impact. | Medium Infrequent event. May only happen occasionally (less than once per year). Has been observed in similar circumstances. 10 to 50% chance of occurring.
Low | Low P First aid injury. E Minor lead, non toxic fugitive emission. A Low repair cost (typically <$10k). Pr Brief interruption or minor quality deviation or minor cost to correct. | Low Unlikely event. Never happened to date. Has never been observed but is still felt to be a possibility Less than 10% chance of occurring.
Notes: 6

## Slide 7
L, M, H Consequence
Risk Criteria Table:
7
Chapter 2.5 What is an Acceptable Level of Risk?
Notes: 7

## Slide 8
L, M, H Likelihood
Risk Criteria Table:
8
Chapter 2.5 What is an Acceptable Level of Risk?
Notes: 8
An activity with a low Likelihood but a high impact on peap, then it results in a medium risk

## Slide 9
Simple Risk Matrix: relates to the Risk Criteria Table, and demonstrates the relationship that Risk is a function of Consequence x Likelihood, and categorizes the risk level.
Risk Matrix:
9
Chapter 2.5 What is an Acceptable Level of Risk?
Notes: 9
Risk level is based on the risk criteria.
Increasing likelihood increases the risk level.
Increasing consequence increases the risk level.
Risk is a function of likelihood and consequence, and there is a level of risk which is defined as “Low”, “Medium”, or “High”. But these do not yet define what is an acceptable level of risk.

## Slide 10
What does Risk Management Direction Mean?
For any given level of risk for an activity, there must be a decision about the activity based on its risk level (i.e. to proceed or not to proceed).
Risk Matrix:
10
Chapter 2.5 What is an Acceptable Level of Risk?
High means “do not proceed”.
Medium means “do not proceed until further protective measures are applied”.
Low means “proceed with caution”
If deemed too high, management direction will dictate how to reduce risks (likelihood and consequence) for a given activity.
Risk Management Directions:
Notes: 10
Management directions go along with each level.
The decision as to whether the risk level of an activity is acceptable or not, is defined by the management directions for that level of risk.
How can you reduce the risks to an acceptable level?

## Slide 11
Up to interpretation; depends on risk tolerance of the organization.
Every organization will have a set of Management Directions.
You will need to explain and apply for your future organization!
“Organization A” “Organization “B”
Management Direction:
11
Chapter 2.5 What is an Acceptable Level of Risk?
Low means readily proceed
Medium means proceed with caution (ensure safeguards are adequate and implemented)
High means do not proceed; take action to reduce risk if possible.
Low means proceed with caution
Medium means do not proceed until additional control measures are implemented.
High means do not proceed.
Notes: 11
Up to some interpretation
Different risk profiles
Mgmt directions may be expressed differently from company to company
But all reduce the risk to an acceptable level in order to proceed

## Slide 12
Example: Apply Risk Management Direction
12
Chapter 2.5 What is an Acceptable Level of Risk?
What is Our Decision?
Scenario: of liquefied propane gas through a flexible transfer hose from storage tank to truck (an acceptable transfer).
Using Risk Criteria table: “has been observed in similar circumstances”, and “could result in a disabling injury or fatality, a toxic/flammable release, etc.”
From the table: Consequence = High, Likelihood = Medium
Therefore ….
Risk is “High”
And
“Do NOT Proceed”
Do Not Proceed
Notes: 12

## Slide 13
Example: Apply Risk Management Direction
13
Chapter 2.5 What is an Acceptable Level of Risk?
What Does This Mean about Our Business Activity?
We are in the business of storing, transferring, and shipping LPG, so …. do all LPG transfers need to cease?
What needs to happen in order for the activity to proceed?
We simply cannot shut down our business, right?
What should we do?
Do Not Proceed
Notes: 13

## Slide 14
Example: Apply Risk Management Direction
14
Chapter 2.5 What is an Acceptable Level of Risk?
What should we do?
What should the management direction be?
How do you reduce the risk to an acceptable level?
How do you decrease the likelihood and/or consequence of an activity?
So you have reduced the risk: Now what?
“Residual Risk” is the (acceptable) level of risk ‘left over’ after controls have been put in place.
Needs to be managed on an ongoing basis.
OK to Proceed
Notes: 14

## Slide 15
We evaluate risk to reduce PEAP losses and increase profitability
We use tools such as risk matrices and risk criteria tables to assess the level of risk from an activity.
If deemed too high, management direction will dictate how to reduce risks (hazard, likelihood, consequence) for a given activity to a level acceptable to the organization, or discontinue the activity if not acceptable.
The level of risk after control measures have been applied to reduce the risk to an acceptable level is termed the “residual risk”.
Summary and Key Lessons:
15
Chapter 2.5 What is an Acceptable Level of Risk?
Notes: 15