## Slide 1
On Becoming a Leader in Risk Management
ENGG404 - Lecture
Chapter 4.1: The Work Processes: Incident Investigation, Root Cause Analysis, and Managing Corrective Actions
At Instructor’s discretion, tee-up video:
“Elementary – Sherlock Holmes and Dr. Watson at the Scene of an Aircraft Crash”
Fundamentals of RM
RM System and Process
Application and Perspectives
People & Org.
Incident Investigation
RM Tools & Challenges
Leadership in RM
RM in Industry

## Slide 2
Explain the need to investigate the scene and collect evidence.
Explain and apply the general II-RCA-MCA Work Process to lead an Incident Investigation immediately after an incident happens, through the RCA and MCA work processes, and to conclude with a final check on the effectiveness of the process.
Learning Outcomes:
‹#›
Chapter 4.1: II-RCA-MCA Work Processes
Notes: ‹#›

## Slide 3
Incidents do happen. If the causes leading to an incident are not addressed, the incident can potentially repeat itself.
Most organizations have systems in place for incident investigation and follow-up.
This lecture presents a framework for the overall work process for Incident Investigation (II), Root Cause Analysis and to Manage the (proposed) Corrective Actions.
Tools for analysis that we will see in the following lectures include Root Cause Analysis (RCA), Cause and Effect Models (C&E), and Manage Corrective Actions (MCA).
Introduction:
‹#›
Chapter 4.1: II-RCA-MCA Work Processes
Notes: ‹#›

## Slide 4
Overall II-RCA-MA Work Process (general workflow):
‹#›
Chapter 4.1: II-RCA-MCA Work Processes
Incident Investigation: collect evidence relating to an event (i.e. the discovery and ascertainment of the facts of a loss incident).
Incident Happens
Incident Investigation
Root Cause Analysis
Check Process Effectiveness
Manage Corrective Actions
Root Cause Analysis (RCA): determine the causes of an incident.
Manage Corrective Actions: manages the corrective and preventative actions that address the latent causes identified in the RCA
Notes: ‹#›

## Slide 5
Detailed II-RCA-MA Work Process (typical):
‹#›
Chapter 4.1: II-RCA-MCA Work Processes
Incident Happens
Investigate?
Appraise situation
Start collecting evidence
All details known?
Conduct the
Root Cause Analysis
Reach conclusions
Report and Communicate
Check effectiveness of the Investigation Process
yes
yes
no
no
Stop
Follow-up to a conclusion
Make Recommendations
Continue collecting evidence
Pick Team
Notes: ‹#›

## Slide 6
Why should I learn how to …?
‹#›
Chapter 4.1: II-RCA-MCA Work Processes
Q: Why should I learn how to investigate incidents, conduct a root cause analysis, and manage corrective actions?
A: It is an essential leadership process!
You will likely need it in your job: you will make decisions of technical and administrative nature in the future.
Because all incidents are preventable and we need to prevent them from recurring that is your role as a leader in risk management!
In your future role as a leader, you will recognize the effectiveness of applying these work processes in shaping the culture of your organization.
Therefore:
Investigation is source for learning (proactive).
Must determine the root causes to prevent recurrence (reactive).
Conduct investigations with a sense of urgency and a sense of commitment!
Notes: ‹#›

## Slide 7
When should you investigate an incident? (Leading organisations)
When it must be reported to the government as required by law.
Whenever there is an incident with consequences (impacts on PEAP).
When there is some value or lesson to be learned from an incident even if there were no consequences.
Can all incidents be investigated?
Most likely not all incidents can be investigated and managed, so how do you choose which incidents to investigate?
Investigations require resources.
Need to define “threshold criteria” in order to assign and use resources effectively!
Challenges:
Some organizations: may do nothing except the bare minimum as may be required by law.
Others have explicit criteria as to what requires an investigation.
Can only investigate when an incident is reported – strong culture that encourages reporting
Incidents Investigated (or Managed) Using this Work Process:
‹#›
Chapter 4.1: II-RCA-MCA Work Processes
Notes: ‹#›
Immediately afterward
Severity or potential severity

## Slide 8
Impartial leader, familiar with the processes, has credibility.
Investigation Team composition (not involved in the incident):
One or more experts in the incident investigation process and the root cause analysis process
One or more technical experts or specialists familiar with the work process being undertaken
Who Undertakes the Overall II-RCA-MCA Work Process?
‹#›
Chapter 4.1: II-RCA-MCA Work Processes
Notes: ‹#›

## Slide 9
When gathering evidence, time is most important!
Evidence can reveal what happened and how, but evidence can deteriorate, or degrade, or disappear with time.
Preservation of evidence:
Evidence – You Need to Know What Happened and How:
‹#›
Chapter 4.1: II-RCA-MCA Work Processes
Notes: ‹#›
You now may be beginning to realize that unless your organization has some established practices in place the investigation will get off to a bad start. Until Syncrude established call out practices for investigators and “freeze evidence” protocols many investigation teams, formed days after the event, had a “cold trail” to follow. Consider the diagram above.
Evidence is captured in four areas known as the “four P’s”, each evidence type will disappear or become disturbed if not “frozen” or preserved. Position evidence is destroyed in minutes if the first people on the scene are unaware of preservation techniques, therefore it is important that the scene is taped off immediately after an incident and entry restricted. People talk amongst themselves and modify their observations accordingly or even forget “short term” memory information, therefore a simple statement sheet can be handed to them immediately after the incident to record their observations. Parts will be disturbed or thrown away, fracture surfaces contaminated. Computer generated data will not be printed and “second” data will be averaged out to “minute” data if practices are not established to dump data to hard copy. So it is important that an organization trains personnel in retention techniques and has established practices for evidence capture.

## Slide 10
A Cat D12 dozer has gotten stuck in unexpected soft and wet clay.
The operator is all right, but the dozer requires repairs (down time).
A broken water pipe was found adjacent to the dozer. The dozer was within its planned route and the area had just been regraded.
Example: The Caterpillar D12 Dozer Loss Incident
‹#›
Chapter 4.1: II-RCA-MCA Work Processes
Notes: ‹#›

## Slide 11
Specialists on the Loss Incident Investigation Team (and rationale):
ESRM II-RCA Expert
Guides the team through the work processes
Dozer Operator(s) NOT involved in the LI
Expertise in operations but NOT personally at stake
Supervisor of the Dozer Operator(s)
Has responsibility (and is accountable) for the dozer operators
Civil / Works Engineer
Expertise for the plot plans / drawings / underground services and surveys
Site / Project Manager
Has overall site/project responsibility, accountable for the loss incident
Dozer operator involved in the LI
as a witness / to be interviewed, but NOT as a member of the team
Surveyor who marked the route and services
as a witness / to be interviewed, but NOT as a member of the team
Why not these two individuals?
Example: The Caterpillar D12 Dozer Loss Incident
‹#›
Chapter 4.1: II-RCA-MCA Work Processes
Notes: ‹#›

## Slide 12
Evidence that should be collected and in the priority order:
Detailed photographs of the scene
Locations of the flagging of the planned route
Locations of the flags marking the underground waterline
People interviews
Mechanical parts
FLRA's
Procedure for the planned route
Underground drawings
Weather bulletins
Why? …because the evidence can “decay” or “degrade” as time passes:
The site and location flags can be disturbed.
People’s memories can fade or be influenced.
Parts?
FLRA’s first, then other documents are less likely to be tampered
Example: The Caterpillar D12 Dozer Loss Incident
‹#›
Chapter 4.1: II-RCA-MCA Work Processes
Notes: ‹#›

## Slide 13
These processes will be effective only if all components are complete, accurate, and thorough.
Process is a learning experience for all.
Must commit to the process with people and resources for investigations.
Summary and Key Lessons:
‹#›
Chapter 4.1: II-RCA-MCA Work Processes
Notes: ‹#›