## Slide 1
On Becoming a Leader in Risk Management
ENGG404 - Lecture
Chapter 6.1: Introduction to Technical Safety and Avoiding Catastrophic Loss Incidents
Fundamentals of RM
RM System and Process
Application and Perspectives
People & Org.
Incident Investigation
RM Tools & Challenges
Leadership in RM
RM in Industry

## Slide 2
Explain two different types of loss incidents, and the differences:
Occupational Safety LI
Technical Safety LI
  Process Safety is a sub-set of Technical Safety
Explain technical safety loss incidents and incident investigations in the context of other engineering disciplines i.e. the catastrophic loss incident.
Apply the concept of technical safety to an industrial example.
Learning Outcomes:
2
Chapter 6.1: Intro to Technical Safety & Avoiding Catastrophic Loss Incidents
Notes: 2

## Slide 3
Two different types of safety concerns:
Occupational Safety generally refers to the prevention of worker injuries, such as prevention of trips, slips and falls.
Technical Safety includes the prevention of loss of control or an unintentional releases of some form of energy. Process Safety is a specialized sub-set.
Thus it follows that there are two different types of loss incidents:
Occupational Safety LI:
Technical Safety LI:
Loss of control
Loss of integrity of the design intent of the engineered system
Unintentional or uncontrolled release of some form of energy
Extremely low likelihood but with catastrophic consequences!
Note that most government agencies do NOT differentiate between these two kinds of loss incidents – any injury in the workplace regardless of the nature of the loss incident is classified as an “occupational injury”.
Different Types of Safety Concerns and LIs:
3
Chapter 6.1: Intro to Technical Safety & Avoiding Catastrophic Loss Incidents
Notes: 3

## Slide 4
Technical Safety Hazard:
Definition - typical “technical hazard” or “technical safety hazard” that may lead to a “technical safety loss incident”:
  Asset: Physical situation where the activity is taking place (i.e. the facility, equipment)
  Potential Impact: Harm or damage to PEAP
  Trigger: A loss of control that resulted in a release of energy
  Energy Source: Nature of energy or nature of materials (shock hazard, momentum/motion, flammable, combustible, etc.)
The general definition of a technical safety hazard and the two incident models lead to an understanding that “technical safety” is NOT limited to chemical unit process operations i.e. any “catastrophic loss incident”!
Technical Safety Hazard and The Incident Models:
4
Now, recall the two Incident Models, the Discovery Approach and relate these to any catastrophic loss incident!
Chapter 6.1: Intro to Technical Safety & Avoiding Catastrophic Loss Incidents
Notes: 4

## Slide 5
Applications of Technical Safety:
Incident: “Crane collapsed, crushing people below crane”
Definition: “technical safety hazard”:
  Asset: ?
  Potential impact: ?
  Trigger: ?
  Energy Source: ?
Discovery Approach:
  Energy Source?
  Triggering Event?
  Line-of-Fire?
  No Safeguard?
Example: Technical Safety, RCA, & The Discovery Approach:
5
Crane collapsed, crushing people below crane
?
?
?
Energy Source: ?
Triggering Event: ?
Line-of-Fire:
?
?
No Safeguard:
?
Chapter 6.1: Intro to Technical Safety & Avoiding Catastrophic Loss Incidents
Notes: 5

## Slide 6
Discovery Approach:
  Energy Source?
  Triggering Event?
  Line-of-Fire?
  No Safeguard?
Applications of Technical Safety:
Incident: “Crane collapsed, crushing people below crane”
Typical “technical safety hazard” definition:
  Asset: crane
  Potential impact: people crushed
  Trigger: Wind loading exceeds specifications
  Energy Source: Gravity
Technical Safety, RCA, and The Discovery Approach:
6
Crane collapsed, crushing people below crane
Crane fell to ground level
Wind forces exceeded crane strength
People were below the crane
Energy Source: gravity
Triggering Event: excessive wind loads
Line-of-Fire:
People below crane
Barriers did not keep people out of area
No Safeguard:
Barriers not in place
Indeed, a crane collapse is a catastrophic LI akin to a refinery explosion.
Chapter 6.1: Intro to Technical Safety & Avoiding Catastrophic Loss Incidents
Notes: 6

## Slide 7
Loss of Containment:
Tailings from a tailings pond
Sewage from a sludge line
Private / secured data breach
Hydrocarbons from a train car
Slope failure of a quarry or roadway
Loss of Integrity of Eng’d Systems:
Aerospace: Boeing 737MAX, STS Challenger & Columbia
Marine: off-shore BP-DWH
Civil: Bridges, buildings, dams, cranes
Transportation: Train derailments
Automotive / Computer Process Control: Takata airbags, Tesla self-driving vehicles
The loss of the integrity of the engineered system that would have the equivalent magnitude or impact of a “process safety loss incident” i.e. an equivalent catastrophic failure!
Technical Safety – Not Just for Chemical Engineers!
7
Chapter 6.1: Intro to Technical Safety & Avoiding Catastrophic Loss Incidents
Notes: 7

## Slide 8
All fields of engineering involved in Process Safety LIs!
Investigations require expertise of many engineering disciplines (mechanical, civil, electrical, etc.)
Process Safety Management and specialized risk assessments require expertise: Design, Constructability, Operability, Maintenance, Process Control, Fire Protection, and so on.
Process Safety – Not Just for Chemical Engineers!
8
Chapter 6.1: Intro to Technical Safety & Avoiding Catastrophic Loss Incidents
Notes: 8

## Slide 9
The potential immediate causes of process safety incidents are innumerable:
“Normalization of Deviance”
Immediate Causes of Process Safety Loss Incidents
9
Not addressing process equipment that is in imminent failure mode, a sub-standard condition.
Tolerance for substandard practices for critical procedures.
Bypassing alarms or taking control systems offline.
Chapter 6.1: Intro to Technical Safety & Avoiding Catastrophic Loss Incidents
Notes: 9

## Slide 10
Small Diameter Tubing – Industrial / Refinery Installations:
Consider small-diameter process tubing that is commonly used in many industrial process unit operations, as depicted here.
10
Chapter 6.1: Intro to Technical Safety & Avoiding Catastrophic Loss Incidents
Notes: 10

## Slide 11
Incident 1:
Caused by ½-inch stainless steel tube between a heat transfer fluid (antifreeze, combustible) pump and a process vessel failed at a fitting near the process vessel.
The resulting leak sprayed onto a re-boiler, very hot surfaces, and ignited causing significant equipment damage.
The tubing failure was the result of uncontrolled vibration the pump.
Incident 2:
Gas leak from ½-inch tubing for pump seal was detected during LNG (Liquefied Natural Gas) plant startup.
Deficient repairs done by unqualified technician.
When the plant re-started, tubing failed completely causing an LNG leak and fire.
As the engineer responsible for these LI’s, what would you do?
Two Incidents Involving Tubing Failure:
11
Chapter 6.1: Intro to Technical Safety & Avoiding Catastrophic Loss Incidents
Notes: 11

## Slide 12
What should we do?
Tubing may not be as durable as pipe and may be more easily damaged.; therefore, avoid impacts to tubing and tubing connections.
Report damaged or leaking tubing observed in the plant and repair it. Report & correct sub-standard conditions i.e. “see it - own it – solve it”.
For design, installation, operation, maintenance:
Follow procedures for tubing identification and isolation for work.
Review procedures for installation, inspection, & maintenance of tubing.
Use qualified personnel to install and repair tubing.
Use correct tools for installation and maintenance of tubing.
Use correct components – tubing, ferrules, nuts, and fittings - do not mix components from different manufacturers.
Ask your tubing supplier to provide information on proper installation and maintenance of their product.
But it is not just about “using the right technology” …
Use your leadership skills to actively practice your technical safety expertise to demonstrate commitment and set the example!
Two Incidents Involving Tubing Failure:
12
Chapter 6.1: Intro to Technical Safety & Avoiding Catastrophic Loss Incidents
Notes: 12

## Slide 13
Sub-standard conditions can be found during inspections on:
For instrument fluid connections: To flush pump and agitator seals, for other applications with small flow requirements e.g. density meters
For conduit connections: instrument signals, electrical power supply
Example: improper assembly
Triggering events:
vibration fatigue failure; misalignment stress – forced fit or struck by; wrong fitting loosened (also a sub-standard practice)
Release of Energy:
Fluid or electricity!
13
Example: Mechanical Integrity of Tubing
Chapter 6.1: Intro to Technical Safety & Avoiding Catastrophic Loss Incidents
Notes: 13

## Slide 14
Differences between Occupational Safety LI and Technical Safety LI:
  Magnitude of the impacts on PEAP as technical safety incidents are typically at least an order of magnitude worse than occupational safety incidents.
  Occupational Safety LI: a worker was injured during the course of physical labour
  Technical Safety LI: loss of control i.e. loss of the integrity of the design intent of the engineered system; this usually results in a catastrophic LI
  Process Safety is a specific sub-set of Technical Safety; process safety management is about keeping hazardous substances contained and/or controlled (prevention of release, mitigation in event of a release).
  Catastrophic LI’s are NOT unique to the chemical process industries.
  Technical safety and process safety are not just for chemical engineers!
An investigation into any technical safety incident requires the expertise of various engineering disciplines (mechanical, civil, electrical, etc.)
Summary and Key Lesson:
14
Chapter 6.1: Intro to Technical Safety & Avoiding Catastrophic Loss Incidents
Notes: 14

## Slide 15
Complete Slide Deck follows with details.
15
Notes: 15

## Slide 16
Explain two different types of loss incidents, and the differences:
Occupational Safety LI
Technical Safety LI
  Process Safety is a sub-set of Technical Safety
Explain technical safety loss incidents and incident investigations in the context of other engineering disciplines i.e. the catastrophic loss incident.
Apply the concept of technical safety to an industrial example.
Learning Outcomes:
16
Chapter 6.1: Intro to Technical Safety & Avoiding Catastrophic Loss Incidents
Notes: 16

## Slide 17
Two different types of safety concerns:
Occupational Safety generally refers to the prevention of worker injuries, such as prevention of trips, slips and falls.
Technical Safety includes the prevention of unintentional releases of some form of energy.
Process Safety is a specialized sub-set of Technical Safety
Thus it follows that there are two different types of loss incidents:
Occupational Safety LI:
An injury to a worker usually caused by an action of that worker or another worker during their work activity e.g. using a sharp blade to cut insulation; standing behind a truck to direct it while backing up; falling from elevation; tripping over materials in a cluttered, unkempt workplace; mishandling of materials
Could be caused by a sub-standard work practice or condition on a small scale.
Breadth of injuries generally limited to 1 or a few persons with rare impacts on E, A, or Pr.
Different Types of Safety Concerns and LIs:
17
Chapter 6.1: Intro to Technical Safety & Avoiding Catastrophic Loss Incidents
Notes: 17

## Slide 18
It follows that there are two different types of loss incidents:
Technical Safety LI:
A loss incident caused by a loss of integrity of the design intent of the engineered system.
This loss of integrity could cause the unintentional or uncontrolled release of some form of energy e.g. chemicals / hazardous substances, thermal, explosive, combustive, electrical, momentum energy, gravity, potential energy, nuclear, radioactive, and so on.
The likelihood of these types is extremely low.
These types of LI’s usually result in catastrophic consequences e.g. tens or more of people, potential major impact on the environment, major loss of assets, and major interruption of business interests.
A “Process Safety LI” is specific to the chemical process operations, and is usually the result of a loss of containment of a hazardous substance.
Some jurisdictions have specific and prescriptive definitions for “what is a process safety loss incident” e.g. US-OSHA defines the release of 5 kg or more of chlorine as a process safety loss incident.
Note that most government agencies do NOT differentiate between these two kinds of loss incidents – any injury in the workplace regardless of the nature of the loss incident is classified as an “occupational injury”.
Different Types of Safety Concerns and LIs:
18
Chapter 6.1: Intro to Technical Safety & Avoiding Catastrophic Loss Incidents
Notes: 18

## Slide 19
Technical Safety Hazard:
Definition - typical “technical hazard” or “technical safety hazard” that may lead to a “technical safety loss incident”:
  Asset: Physical situation where the activity is taking place (i.e. the facility, equipment)
  Potential Impact: Harm or damage to PEAP
  Trigger: A loss of control that resulted in a release of energy
  Energy Source: Nature of energy or nature of materials (shock hazard, momentum/motion, flammable, combustible, etc.)
The general definition of a technical safety hazard and the two incident models lead to an understanding that “technical safety” is NOT limited to chemical unit process operations i.e. any “catastrophic loss incident”!
Technical Safety Hazard and The Incident Models:
19
Now, recall the two Incident Models, the Discovery Approach and relate these to any catastrophic loss incident!
Chapter 6.1: Intro to Technical Safety & Avoiding Catastrophic Loss Incidents
Notes: 19

## Slide 20
Applications of Technical Safety:
Incident: “Crane collapsed, crushing people below crane”
Definition: “technical safety hazard”:
  Asset: ?
  Potential impact: ?
  Trigger: ?
  Energy Source: ?
Discovery Approach:
  Energy Source?
  Triggering Event?
  Line-of-Fire?
  No Safeguard?
Example: Technical Safety, RCA, & The Discovery Approach:
20
Crane collapsed, crushing people below crane
?
?
?
Energy Source: ?
Triggering Event: ?
Line-of-Fire:
?
?
No Safeguard:
?
Chapter 6.1: Intro to Technical Safety & Avoiding Catastrophic Loss Incidents
Notes: 20

## Slide 21
Discovery Approach:
  Energy Source?
  Triggering Event?
  Line-of-Fire?
  No Safeguard?
Applications of Technical Safety:
Incident: “Crane collapsed, crushing people below crane”
Typical “technical safety hazard” definition:
  Asset: crane
  Potential impact: people crushed
  Trigger: Wind loading exceeds specifications
  Energy Source: Gravity
Technical Safety, RCA, and The Discovery Approach:
21
Crane collapsed, crushing people below crane
Crane fell to ground level
Wind forces exceeded crane strength
People were below the crane
Energy Source: gravity
Triggering Event: excessive wind loads
Line-of-Fire:
People below crane
Barriers did not keep people out of area
No Safeguard:
Barriers not in place
Indeed, a crane collapse is a catastrophic LI akin to a refinery explosion.
Chapter 6.1: Intro to Technical Safety & Avoiding Catastrophic Loss Incidents
Notes: 21

## Slide 22
Loss of Containment:
Tailings from a tailings pond
Sewage from a sludge line
Private / secured data breach
Hydrocarbons from a train car
Slope failure of a quarry or roadway
Loss of Integrity of Eng’d Systems:
Aerospace: Boeing 737MAX, STS Challenger & Columbia
Marine: off-shore BP-DWH
Civil: Bridges, buildings, dams, cranes
Transportation: Train derailments
Automotive / Computer Process Control: Takata airbags, Tesla self-driving vehicles
The loss of the integrity of the engineered system that would have the equivalent magnitude or impact of a “process safety loss incident” i.e. an equivalent catastrophic failure!
Technical Safety – Not Just for Chemical Engineers!
22
Chapter 6.1: Intro to Technical Safety & Avoiding Catastrophic Loss Incidents
Notes: 22

## Slide 23
All fields of engineering involved in Process Safety LIs!
Process safety incident investigations require expertise of many engineering disciplines (mechanical, civil, electrical, etc.)
Need to conduct a robust and thorough investigation
The key concern with a process safety incident is that the magnitude of the loss is significantly higher than occupational safety incident.
Process Safety – Not Just for Chemical Engineers!
23
Chapter 6.1: Intro to Technical Safety & Avoiding Catastrophic Loss Incidents
Notes: 23

## Slide 24
All fields of engineering involved in Process Safety LIs!
Process safety management requires expertise in all elements in a risk management program for reviews (risk assessments), throughout all stages (Design, Constructability, Operability, Maintenance) and all engineering disciplines (mechanical, civil, electrical, process control, fire protection, and so on).
Process Safety – Not Just for Chemical Engineers!
24
Chapter 6.1: Intro to Technical Safety & Avoiding Catastrophic Loss Incidents
Notes: 24

## Slide 25
The potential immediate causes of process safety incidents are innumerable:
If these causes are not checked and corrected, “Normalization of Deviance” creeps into the organization.
Immediate Causes of Process Safety Loss Incidents
25
Not addressing process equipment that is in imminent failure mode, a sub-standard condition.
Tolerance for substandard practices for critical procedures.
Bypassing alarms or taking control systems offline.
Chapter 6.1: Intro to Technical Safety & Avoiding Catastrophic Loss Incidents
Notes: 25

## Slide 26
Small Diameter Tubing – Industrial / Refinery Installations:
Consider small-diameter process tubing that is commonly used in many industrial process unit operations, as depicted here.
26
Chapter 6.1: Intro to Technical Safety & Avoiding Catastrophic Loss Incidents
Notes: 26

## Slide 27
Incident 1:
Caused by ½-inch stainless steel tube between a heat transfer fluid (antifreeze, combustible) pump and a process vessel failed at a fitting near the process vessel.
The resulting leak sprayed onto a re-boiler, very hot surfaces, and ignited causing significant equipment damage.
The tubing failure was the result of uncontrolled vibration the pump.
Incident 2:
Gas leak from ½-inch tubing for pump seal was detected during LNG (Liquefied Natural Gas) plant startup.
Deficient repairs done by unqualified technician.
When the plant re-started, tubing failed completely causing an LNG leak and fire.
As the engineer responsible for these LI’s, what would you do?
Two Incidents Involving Tubing Failure:
27
Chapter 6.1: Intro to Technical Safety & Avoiding Catastrophic Loss Incidents
Notes: 27

## Slide 28
What should we do?
Tubing may not be as durable as pipe and may be more easily damaged.; therefore, avoid impacts to tubing and tubing connections.
Report damaged or leaking tubing observed in the plant and repair it. Report & correct sub-standard conditions i.e. “see it - own it – solve it”.
For design, installation, operation, maintenance:
Follow procedures for tubing identification and isolation for work.
Review procedures for installation, inspection, & maintenance of tubing.
Use qualified personnel to install and repair tubing.
Use correct tools for installation and maintenance of tubing.
Use correct components – tubing, ferrules, nuts, and fittings - do not mix components from different manufacturers.
Ask your tubing supplier to provide information on proper installation and maintenance of their product.
But it is not just about “using the right technology” …
Use your leadership skills to actively practice your technical safety expertise to demonstrate commitment and set the example!
Two Incidents Involving Tubing Failure:
28
Chapter 6.1: Intro to Technical Safety & Avoiding Catastrophic Loss Incidents
Notes: 28

## Slide 29
Sub-standard conditions can be found during inspections on:
For instrument fluid connections: To flush pump and agitator seals, for other applications with small flow requirements e.g. density meters
For conduit connections: instrument signals, electrical power supply
Example: improper assembly
Triggering events:
vibration fatigue failure; misalignment stress – forced fit or struck by; wrong fitting loosened (also a sub-standard practice)
Release of Energy:
Fluid or electricity!
29
Example: Mechanical Integrity of Tubing
Chapter 6.1: Intro to Technical Safety & Avoiding Catastrophic Loss Incidents
Notes: 29

## Slide 30
Differences between Occupational Safety LI and Technical Safety LI:
  Magnitude of the impacts on PEAP as technical safety incidents are typically at least an order of magnitude worse than occupational safety incidents.
  Occupational Safety LI: a worker was injured during the course of physical labour
  Technical Safety LI: loss of control i.e. loss of the integrity of the design intent of the engineered system; this usually results in a catastrophic LI
  Process Safety is a specific sub-set of Technical Safety; process safety management is about keeping hazardous substances contained and/or controlled (prevention of release, mitigation in event of a release).
  Catastrophic LI’s are NOT unique to the chemical process industries.
  Technical safety and process safety are not just for chemical engineers!
An investigation into any technical safety incident requires the expertise of various engineering disciplines (mechanical, civil, electrical, etc.)
Summary and Key Lesson:
30
Chapter 6.1: Intro to Technical Safety & Avoiding Catastrophic Loss Incidents
Notes: 30