## Slide 1
On Becoming a Leader in Risk Management
ENGG404 - Lecture
Chapter 3.3: The Risk Management System and Elements
Part 2
Fundamentals of RM
RM System and Process
Application and Perspectives
People & Org.
Incident Investigation
RM Tools & Challenges
Leadership in RM
RM in Industry

## Slide 2
Explain the risk management system elements in more detail including relevant, real-world examples as points of references, and typical latent cause statements.
Although all 11 elements are listed in this presentation, only these three are discussed in detail in the lecture:
1) Management Leadership, Commitment, and Accountability
5) Incident Reporting, Investigation, Analysis and Actions:
6) Program Evaluation and Continuous Improvement:
Learning Outcomes:
2
Chapter 3.3: The Risk Management System & its Elements
Notes: 2

## Slide 3
Risk Management System (APEGA Model):
Management Leadership, Commitment and Accountability (MLCA)
Risk Assessment and Management of Risks (RAMR)
Community Awareness and Emergency Preparedness (CAEP)
Management of Change (MOC)
Incident Reporting, Investigation, Analysis and Actions (IRIAA)
Program Evaluation and Continuous Improvement (PECI)
Design, Construction and Start-up (DCSU)
Operations and Maintenance (OM)
Employee Competency and Training (ECT)
Contractor Competency and Integration (CCI)
Operations and Facilities Information and Documentation (OFID)
A Model of the Risk Management System:
3
Chapter 3.3: The Risk Management System & its Elements
Be able to explain and apply each of these elements!
Notes: 3

## Slide 4
All 11 of the RMS elements relate to the Engineer’s Survival Guide:
        #1: Understand company values.
        #2: Understand your program.
        #3: When you make decisions, put safety ahead of any other objective!
        #4: Pay attention to failures in safety systems and take action.
          Thinking back to the previous topic, The Swiss Cheese Model and the case of the “loading operation with the defective level switch”, what “safety systems” can you identify?
Introduction:
4
Chapter 3.3: The Risk Management System & its Elements
Notes: 4

## Slide 5
As you will learn in the application of the fourth key point of The Engineer’s Survival Guide, “failures in safety systems” can include:
Administrative Controls: in this case, a procedure for prioritizing did not escalate the priority and allocation of resources to repair the defective limit switch, which obviously is a device necessary to prevent overfilling the rail-car.
Engineering Controls: In this case, the level switch and its “high level alarm / flow shut-off” feature are not working; this hardware safety system deosn not detect a high level condition, does not annunciate a “high level” alarm, and does not shut-off the flow of the combustible fluid to the rail-car
RM Programs: In this case, the maintenance program to maintain and repair instrumentation did not include a standard to classify “priority” repairs on critical level instrumentation.
Introduction:
5
Chapter 3.3: The Risk Management System & its Elements
        The Engineer’s Survival Guide:
        #4: Pay attention to failures in safety systems and take action.
          Thinking back to the previous topic, The Swiss Cheese Model and the case of the “loading operation with the defective level switch”, what “safety systems” can you identify?
Notes: 5

## Slide 6
If weaknesses here, the system will fail or mediocre results at best.
Management sets the culture and tone of the organization
Long term and pro-active commitment
Management actions must be consistent between their words and actions - walk the talk!
Applies their fundamental process of Plan–Do–Check–Act
Is the driver of PDCA
Example: A worker did not follow the ‘back in’ parking procedure at a job site because his supervisor never communicated the importance of following the company’s safety procedures.
Example: A worker did not follow the ‘back in’ parking procedure at a job site even though his supervisor communicated the importance of following the company’s safety procedures. The supervisor sees what the employee has done, and she discusses the issue with the worker.
It’s what this course is all about! For your team project:
Did the engineer or management prioritize profit or production over safety when making decisions?
Latent causes are generally expressed as a weakness in (LCs GW:) corporate safety values program, leadership program, or specific components (indoctrinating commitment and accountability in leaders) of same.
Example LC-S: The leadership program did not include a strategy or plan to establish “safety” as a core value and communicate this value to employees.
Explore RME #1) Management Leadership, Commitment & Accountability
6
Chapter 3.3: The Risk Management System & its Elements
Notes: 6
Most important one!!!
Focus on this in chapter 9
What gets measured gets managed

## Slide 7
From the textbook: “A more appropriate name for this element would be Element 2: Risk Assessment and Control of Risks
Hazard Identification, FLRA, SQRA, JSA, Checklists, Reporting & Correcting Substandard Conditions & Practices, Planned Inspections,
Eliminate risks, or reduce and control to an acceptable level.
Example: A worker loaded a standard wheel-barrow cart containing with a heavy load of metal. The worker injured their back while attempting to lift and move the cart. The worker did not apply their FLRA or refer to the JSA at the start of the job; otherwise, the worker would have used the four-wheeled cart for moving heavy loads.
So What Does This Mean for your team project??
Did an engineer / management make a decision or complete a task without recognizing the risk or assessing the risks first?
Did they recognize the risk from the activity or task before completing it? If not, why not?
LCs GW: a risk management program to assess risks and / or a program to actively manage risks to an acceptable level.
Example LC-C: The worker did not comply with the FLRA and JSA (standards) as documented in the risk assessment program.
An improvement on the previous example: LC-C: The requirements of the FLRA and JSA (standards) as documented in the risk assessment program were not met.
Example LC-S: The risk assessment program did not include a standard to assign the roles and responsibilities for foreperson / supervisor oversight on the use of FLRA, JSA’s, and other safe operating / maintenance procedures (SOP’s/SMP’s).
Explore RME #2) Risk Assessment and Management of Risks
7
Chapter 3.3: The Risk Management System & its Elements
Notes: 7

## Slide 8
Community Awareness
Inform stakeholders of hazards, risks, and risk control measures
Emergency Preparedness
Develop potential loss scenarios and plans to mitigate the loss scenarios and practice emergency drills!
Provide and maintain resources (people, equipment, agency coordination)
Example: The fire exit doors at a manufacturing facility were blocked with boxes of product because of a delay in pick up by the shipping company.
Example: Residents living near a refinery don’t know what to do when they hear a siren going off at the refinery.
So What Does This Mean for your team project??
Was there a community in close proximity to the operation i.e. were they aware of the risks?
Was management prepared for an emergency at the facility i.e. was there an emergency plan in place?
LCs GW: a community awareness program and/or an emergency preparedness program.
Example LC-S: The emergency preparedness program did not include a standard for regular inspections of fire exit doors
Example LC-P: The company did not have a community awareness program to communicate facility hazards, siren signals, and what to do when the siren is sounded.
Explore RME #3) Community Awareness and Emergency Preparedness:
8
Chapter 3.3: The Risk Management System & its Elements
Notes: 8

## Slide 9
A change from what has usually or normally been done or used e.g. procedure, or a change in the organization (people and processes)
“Change” introduces or causes a change in: a) risk level, or b) the effectiveness in risk control measures, or c) new risks!
Management must clearly communicate the definition of change, and reinforce the processes for managing change.
Example: An engineer wants to switch out a tank used to store diesel to now store gasoline. The engineer has never done this before. The engineer can’t decide if he should complete a full risk assessment for this change because there are no procedures available to the engineer that detail how this change is to be undertaken.
What does this mean for your team project??
Did an employee make a change to a standard operating procedure?
Did an engineer or contractor make a change to an engineered system (during design, construction, operation, or maintenance) without assessing the risk from the change first? If not, why?
LCs GW: a Management of Change program.
Example LC-S: The management of change program did not include a procedure or review steps for changes to product storage tank.
Explore RME #4) Management of Change: Chapter 3.4
9
Chapter 3.3: The Risk Management System & its Elements
Notes: 9

## Slide 10
Proactive and reactive management action can contribute significantly to improvements in the management system.
Reporting mechanisms are in place for recording and tracking:
  Proactive: incidents without consequences (near miss events) as well as sub-standard conditions and sub-standard practices.
  Reactive: incidents with consequences.
Incidents are investigated, analysed, and corrective actions determined to prevent re-occurrence.
Example: An employee sustains a minor injury while using a defective tool. The worker reports to the First Aid station as per company policy. The supervisor could investigate the incident, file a report, and discuss the incident at the next safety meeting regarding inspection of tools prior to use, but there were no criteria to state what should be investigated i.e. that a minor injury should be investigated.
What does this mean for your team project?
Were incidents and near misses reported?
Did management know about past incidents at the facility?
Was there a plan for responding to reported incidents?
Were corrective actions developed and followed up on?
LCs GW: one or more of the programs / processes of this element; recall our Incident Investigation - Root Cause Analysis - Manage Actions work processes!
Example LC-S: The incident investigation program did not include a standard to describe the threshold criteria for what should be investigated with follow-up action.
Explore RME #5) Incident Reporting, Investigation, Analysis and Actions:
10
Chapter 3.3: The Risk Management System & its Elements
Notes: 10

## Slide 11
Continuous improvement (proactive) is essential to ensure your program and organization are managing the residual risks!
Continually checking each of the program elements, their standards (administrative controls), and the implementation of those standards
Program evaluation works on all parts of the RMS Program:
Audits (internal, external) test implementation of the program at organization level to ensure it is effectively implemented!
Example: A third party firm is hired to do an audit on the safe shut down of a plant. The auditors reviewed the procedures and observed work practices during the shut down. After the audit is completed, the managers at the company discussed the deficiencies found, but did not develop corrective actions, and did not implement any actions to correct the deficiencies.
So What Does This Mean for your team project??
Did management conduct audits to determine the effectiveness of their risk management program, such as comparing administrative controls with actual work practices?
Was management supporting the audit follow-up i.e. take action to correct deficiencies?
LCs GW: an auditing program and its components e.g. schedule, details on what to audit, assignment and commitment to audit.
Example LC-S: The Evaluation Program did not include an audit process (a standard) to check the tracking and implementation of corrective actions as discovered in third-party audits.
Explore RME #6) Program Evaluation and Continuous Improvement:
11
Chapter 3.3: The Risk Management System & its Elements
Notes: 11

## Slide 12
Auditing can be easily confused with monitoring, investigating, and inspecting.
RME #6 PECI IS about auditing to see how effective your:
Safety Program is actually doing what is intended; in other words, “Are you (Management) actually measuring and tracking the leading indicators, reviewing on a routine and scheduled basis, and taking appropriate actions in response to those leading indicators?”
Investigations And The Management Of Actions Program is actually doing what is intended; in other words, “Are your investigations being done correctly and thoroughly, and have any actions been effectively implemented?”
Construction Program is actually doing what is intended; in other words, “Are your inspections being done correctly and thoroughly, and have any installation deviations from design been corrected?”
Maintenance Program is actually doing what is intended; in other words, “Are your inspections being done correctly and thoroughly, and have any repair/maintenance deviations from manufacturer's specifications been corrected?”
Such questions are part of the Evaluation Program with intent for continuous improvement of the Technical Safety Program, the Investigations and the Management of Actions program, the Construction program, and the Maintenance program, respectively.
These are but some of the examples to signify the purpose of RME#6 PECI.
More content will be presented about RME #6 PECI in a later topic.
Explore RME #6) Program Evaluation and Continuous Improvement:
12
Chapter 3.3: The Risk Management System & its Elements
Notes: 12

## Slide 13
Links project planning, project management, and project execution (from the conceptual stage to the hand over and start-up stage) with appropriate risk assessment reviews (RME #2)
Is risk management designed into the engineered system?
Is risk management built into the engineered system? Are the control measures confirmed effective during commissioning and start-up?
Example: A wheeled cart containing heavy equipment tipped over and injured a worker. The cart tipped over because the caster wheels on the cart were too small. The engineer who designed the cart chose inappropriately sized casters for the height and weight of the cart because she didn’t use the available design standard when choosing the casters for heavy loads.
So What Does This Mean for your team project??
Were there design components that needed a risk assessment?
Did the engineer recognize that certain aspects of the design needed a risk assessment or needed a more in-depth RA?
LCs GW: a design program, a construction program, or a start-up program.
Example LC-C: The designer did not comply with the design standards for sizing and selecting caster wheels as documented in the equipment design program.
An improvement on the previous example: LC-C: The requirements of the design standards for sizing and selecting caster wheels as documented in the equipment design program were not met.
Example LC-S: The design program did not include a standard to assign roles and responsibilities for senior oversight of a junior’s use of standards for cart design.
Explore RME #7) Design, Construction, and Start-up:
13
Chapter 3.3: The Risk Management System & its Elements
Notes: 13

## Slide 14
Encompasses the establishment of criteria for operating and maintaining the facility, and all related activities.
Facilities must be operated and maintained within established criteria i.e. “The Maintenance Manual”, “The Operating Manual”
The monitoring, recording, and the analysis of records will reveal deteriorating or deviating conditions that need to be addressed; thus proactively preventing an incident.
Example: An employee wants to lock out and tag a broken piece of equipment on the robotic packaging line for repair, but the operating procedure in the manual lacks detail on what valves, electrical switches, and mechanical interlocks to lock out.
What does this mean for your team project??
Did the organization have established requirements for O&M that were adequate for the level of activity risk?
Was the organization proactive in monitoring & addressing “signals” for weaknesses in O&M – such as lack of maintenance, or lack of following administrative controls (procedures, etc.)?
Example LC-S: The shut-down and lock-out standard in the operations program did not list which valves, switches, and interlocks to lock-out / tag-out for the robotic packaging line.
Explore RME #8) Operations and Maintenance:
14
Chapter 3.3: The Risk Management System & its Elements
Notes: 14

## Slide 15
Encompasses “core employees”.
Training is an effective method for setting expectations.
Managers are responsible for ensuring their employees are properly trained and certified / qualified.
So What Does This Mean to the Organization?
Training is a form of due diligence.
Example: A wheeled cart containing heavy equipment tipped over because the load was unbalanced. The worker who was using the cart was not trained in how to properly load material into the cart.
What does this mean for your team project??
Were employees adequately trained for the tasks they were performing? Did they need additional training?
Was there an effective training program in place?
LCs GW: a training program, that trains and/or certifies / and/or qualifies and/or recruits employees.
Example LC-S: The employee training program did not include a standard for the cart loading procedures.
Explore RME #9) Employee Competency and Training:
15
Chapter 3.3: The Risk Management System & its Elements
Notes: 15

## Slide 16
Encompasses contract workers whose employer is providing services to the main organization
Managers of the main organization must ensure: i) the contractor companies have properly trained / certified / qualified their employees, and ii) contract workers are appropriately trained & integrated.
Expectations for the main organization’s employees and contract workers should and must be the same. No “double-standard”.
Example: A bridge construction company hired a contractor to oversee the testing of concrete used for a bridge construction project. The construction company did not require the contractor to complete the site safety orientation.
What does this mean for your team project??
Was there an effective training program in place for contractors?
Were contractor organizations screened for safety performance? Were contractors involved in job planning, including risk assessments?
After hiring, did management assess contractor performance?
LCs GW: a program to select / hire contractor companies, and to integrate or indoctrinate those contractor employees into the safety culture and risk management program of the core organization.
Example LC-S: The contractor integration program did not include a standard to require site safety orientation training for contractors working on projects.
Explore RME #10) Contractor Competency and Integration:
16
Chapter 3.3: The Risk Management System & its Elements
Notes: 16

## Slide 17
Establishes how information and documentation – the administrative controls and any records generated – are managed (catalogued, archived, filed, accessed, retrieved, etc.) within a risk management program.
Good information and documentation with ready access is essential for tracking trends and managing administrative controls
Managers must implement appropriate policies and procedures where workers are making decisions based on the information.
Example: An employee is working on a broken piece of equipment, but the drawings and operations / maintenance manual are not readily available.
What does this mean for your team project?
Was the necessary information (such as safety rules and requirements, administrative controls, design drawings, specifications, inspection reports, etc.) kept current?
Was the necessary information readily available for workers?
Were records created from the execution of these administrative controls properly filed / catalogued for future reference?
LCs GW: a program for managing the documentation of information, including the risk management program, of any aspect of the operations / facilities.
Example LC-S: The documentation program did not include a standard that describes how to inventory and catalogue the manufacturer’s drawings and operations / maintenance manual, nor provide ready-reference filing numbers for employees to access these documents.
Explore RME #11) Operations & Facilities Information & Documentation:
17
Chapter 3.3: The Risk Management System & its Elements
Notes: 17

## Slide 18
Although the manager of the facility within an organization is ultimately responsible for effective implementation and execution, various levels of management, various departments, and various “expertise centres” own (effectively manage the implementation of) specific risk management system elements.
RM Element Owners:
18
Chapter 3.3: The Risk Management System & its Elements
Element # | “Owner”
#1 MLC&A | The most senior management for a company, a division, a department, or a facility.
#2 RA&MR | Safety / Risk Engineering, Occupational Health, Job Safety Experts
#3 CA&EP | CA: Public Relations and Communications; EP: Company Emergency Services
#4 MOC | Safety Expertise (safety department)
#5 IRIAA | Safety Expertise (safety department) in Technical Safety or Occupational Safety
#6 PE&CI | Audit Expertise Centre
#7 DC&SU | Engineering, Project Management, Construction Department
#8 O&M | Operating Facilities (Plants); Maintenance Departments
#9 EC&T | Training Department
#10 CC&I | Contractor Management Department
#11 OFID | Document Control (Engineering Files and Records) Department
Notes: 18

## Slide 19
Please confer on these questions: How are RME #1 MLCA & #6 PECI integrated with the “know-how / how-to” (operations) of risk management?
What does #1 MLCA do? What does #6 PECI do? (MM-Poll) (MM-Poll)
How are RMEs #1 and #6 integrated in risk management? (open discussion)
ALE: The APEGA Model – Driver, Evaluation, and Operations:
19
Chapter 3.3: The Risk Management System & its Elements
#1 MLCA
#6 PECI
“OPERATIONS”
#2 Risk Assessment and Management of Risks
#3 Community Awareness and Emergency Preparedness
#4 Management of Change
#5 Incident Reporting, Investigation, Analysis and Actions
#7 Design, Construction and Start-up
#8 Operations and Maintenance
#9 Employee Competency and Training
#10 Contractor Competency and Integration
#11 Operations & Facilities Information & Documentation
Notes: 19

## Slide 20
How #1 MLCA & #6 PECI integrate with the “know-how / how-to” (operations) of risk management:
The APEGA Model – Driver, Evaluation, and Operations:
20
Chapter 3.3: The Risk Management System & its Elements
#1 Management Leadership, Commitment, and Accountability
#6 Program Evaluation and Continuous Improvement
#2 Risk Assessment and Management of Risks
#3 Community Awareness and Emergency Preparedness
#4 Management of Change
#5 Incident Reporting, Investigation, Analysis and Actions
#7 Design, Construction and Start-up
#8 Operations and Maintenance
#9 Employee Competency and Training
#10 Contractor Competency and Integration
#11 Operations and Facilities Information and Documentation
“DRIVER”
“EVALUATION”
“OPERATIONS”
Notes: 20

## Slide 21
As you will discover in your team project RCAs, weaknesses in a risk management system element degrade or disable the organization’s means to manage the residual risks within the scope of control of that element.
Latent cause statements are specific, unique, and directly relate to one RME.
The APEGA Model is a foundational model, but is one of innumerable risk management systems – learn YOUR employer’s system/program! (ESG KP#2)
Summary and Key Lessons:
21
Chapter 3.3: The Risk Management System & its Elements
Risk Management System (APEGA Model):
Management Leadership, Commitment and Accountability (MLCA)
Risk Assessment and Management of Risks (RAMR)
Community Awareness and Emergency Preparedness (CAEP)
Management of Change (MOC)
Incident Reporting, Investigation, Analysis and Actions (IRIAA)
Program Evaluation and Continuous Improvement (PECI)
Design, Construction and Start-up (DCSU)
Operations and Maintenance (OM)
Employee Competency and Training (ECT)
Contractor Competency and Integration (CCI)
Operations and Facilities Information and Documentation (OFID)
Notes: 21

## Slide 22
Any questions?
Notes: 22