## Slide 1
On Becoming a Leader in Risk Management
Chapter 4.5 Linking Latent Causes to Recommendations for Action
Fundamentals of RM
RM System and Process
Application and Perspectives
People & Org.
Incident Investigation
RM Tools & Challenges
Leadership in RM
RM in Industry

## Slide 2
Write an acceptable statement for a latent cause.
Test cause statements to determine category of the cause.
Link a latent cause to a management system element.
Explain how to “make the link” from latent causes to recommendations for actions.
Learning Outcomes:
2
Chapter 4.5: Linking Latent Causes to Recommendations
Notes: 2

## Slide 3
Introduction – The Construct of an RCA:
3
Chapter 4.5: Linking Latent Causes to Recommendations
Incident
Immediate Cause
Intermediate Cause
Basic Cause
Latent Cause
Weakness in Management System Element #.
Engineering Factors Job Factors Personal Factors
Basic Cause
Immediate Cause
Incident Description
Latent Cause
Inadequate Program Inadequate Standards Inadequate Compliance
Recommendation?
Causes in the Root Cause Analysis
Category of Cause
Type of Cause
Substandard Work Practice or Substandard Condition
Intermediate Cause
Notes: 3

## Slide 4
Example: Examine One Root of a Root Cause Analysis:
4
Chapter 4.5: Linking Latent Causes to Recommendations
Equipment found in defective state
Improper Risk Taking Improper Motivation
Basic Cause
Immediate Cause
Incident Description
Latent Cause
Inadequate Program
Causes in the Root Cause Analysis
Category of Cause
Type of Cause
Sub-standard Work Practice
Management failed to communicate or did not check that the IM understood Corporate Values: “Safety always before Production”
IM had not yet learned or taken to heart or cared that or understood that safety checks must be done before Prod’n checks
IM prioritized Mtce work on Prod’n Equipment over Safety Equipment
Industrial Mechanic (IM) did not follow / implement procedure
Latent cause?
What improvement would you make in this cause statement?
What improvement would you make in this cause statement?
Notes: 4
The word “OR” in the cause statements (yellow box and white box) is replaced with an OR gate, and two roots result, per next slide.

## Slide 5
5
Chapter 4.5: Linking Latent Causes to Recommendations
Equipment found in defective state
Industrial Mechanic (IM) did not follow / implement procedure
IM prioritised Mtce work on Prod’n Equipment over Safety Equipment
IM had not yet learned (i.e. cared for, understood) that safety checks must be done before Prod’n checks
IM was not trained on Corporate Values
Mngmt System did not check that the IM understood Corporate Values: “Safety always before Production” as part of the communications plan.
Mngmt System did not train IM on Corporate Values
LC-C: The (existing) training program on Corporate Values was not implemented.
The cause statement on the previous page included the “OR” word, so branch to another root.
State so that you do not imply to ”blame management”.
Instead of “Management failed …”, state “Management did not …” or “Management system did not …”
Example: Examine One Root Splits to Two Roots
Notes: 5
Note the sub-category for the left root latent cause: because the training program exists (the cause states “not implemented”), so one could reasonably infer that this latent cause can be categorized as a “C – Inadequate Compliance with Program Standards”.
Note the sub-category for the right root latent cause: because the communications plan lacked specific steps to check (and validate) training on Corporate Values, one could reasonably infer that the program exists, but the details (standard) were inadequate; thus, this latent cause can be categorized as an “S – Inadequate Program Standards”.

## Slide 6
6
Chapter 4.5: Linking Latent Causes to Recommendations
Equipment found in defective state
Industrial Mechanic (IM) did not follow / implement procedure
IM prioritised Mtce work on Prod’n Equipment over Safety Equipment
IM had not yet learned (i.e. cared for, understood) that safety checks must be done before Prod’n checks
IM was not trained on Corporate Values
Mngmt System did not check that the IM understood Corporate Values: “Safety always before Production” as part of the communications plan.
Mngmt System did not train IM on Corporate Values
LC-C: The (existing) training program on Corporate Values was not implemented.
LC-S: The management communications program did not include steps in the communications plan to check that new employees could explain Corporate Values.
ALE #1: Examine Right Root Latent Cause
Now, please confer: (pen-to-paper / Zoom Chat Open)
Explain why the right root latent cause is categorized as “S – inadequate program standards”.
Notes: 6
Note the sub-category for the left root latent cause: because the training program exists (the cause states “not implemented”), so one could reasonably infer that this latent cause can be categorized as a “C – Inadequate Compliance with Program Standards”.
Note the sub-category for the right root latent cause: because the communications plan lacked specific steps to check (and validate) training on Corporate Values, one could reasonably infer that the program exists, but the details (standard) were inadequate; thus, this latent cause can be categorized as an “S – Inadequate Program Standards”.

## Slide 7
Example: Examine Right Root Latent Cause
7
Chapter 4.5: Linking Latent Causes to Recommendations
Equipment found in defective state
Industrial Mechanic (IM) did not follow / implement procedure
IM prioritised Mtce work on Prod’n Equipment over Safety Equipment
IM had not yet learned (i.e. cared for, understood) that safety checks must be done before Prod’n checks
IM was not trained on Corporate Values
Mngmt System did not check that the IM understood Corporate Values: “Safety always before Production” as part of the communications plan.
Mngmt System did not train IM on Corporate Values
LC-C: The (existing) training program on Corporate Values was not implemented.
This latent cause statement states that there is a program and that the plan is a “standard” (an administrative control) that is missing “steps to check that new employees could explain”; thus, the LC is categorized as “S – inadequate program standards”.
LC-S: The management communications program did not include steps in the communications plan to check that new employees could explain Corporate Values.
Notes: 7
Note the sub-category for the left root latent cause: because the training program exists (the cause states “not implemented”), so one could reasonably infer that this latent cause can be categorized as a “C – Inadequate Compliance with Program Standards”.
Note the sub-category for the right root latent cause: because the communications plan lacked specific steps to check (and validate) training on Corporate Values, one could reasonably infer that the program exists, but the details (standard) were inadequate; thus, this latent cause can be categorized as an “S – Inadequate Program Standards”.

## Slide 8
Recall Best Practices: The Latent Cause Statement
8
Recall the best practices: these examples of latent cause statement have these items in common:
Labelled and numbered: LC1, LC2, etc.
Categorized as P, S, or C, categorizing these with appropriately stated latent causes demonstrates the ability to differentiate among the three categories of latent causes.
Each statement has four components, not always in this order for 3 & 4:
Relates to an element “training”, “design”, “incident reporting”, etc.;
Has the word “program”;
Gives some level or degree of inadequacy that relates to the LC category e.g. inadequate program, inadequate program standards, or inadequate compliance with program standards;
Specific and unique terms or phrases relevant to the root in question.
The stated latent cause then clearly links to a Risk Management System element.
Chapter 4.5: Linking Latent Causes to Recommendations
Notes: 8

## Slide 9
Examine One Root in an RCA: Latent Cause & Recommendation
9
Chapter 4.5: Linking Latent Causes to Recommendations
Equipment found in defective state
Improper Risk Taking Improper Motivation
Basic Cause
Immediate Cause
Incident Description
Latent Cause
Inadequate Standard
Causes in the Root Cause Analysis
Category of Cause
Type of Cause
Sub-standard Work Practice
Mngmt System did not check that the IM understood Corporate Values: “Safety always before Production” as part of the communications plan.
IM had not yet learned (i.e. carunderstood) that safety checks must be done before Prod’n checks
IM prioritized Mtce work on Prod’n Equipment over Safety Equipment
Industrial Mechanic (IM) did not follow / implement procedure
LC-S: The management communications program did not include steps in the communications plan to check that new employees could explain Corporate Values. #1 MLCA
Note the Latent Cause is stated in unique and specific terms relevant to the loss incident RCA and is aligned with RME#1 MLCA. It should be straight-forward to write a recommendation.
Please confer (pen-to-paper / MM-Open):
What would your recommendation be to address this latent cause?
Notes: 9
Note the sub-category for the right root latent cause: because the communications plan lacked specific steps to check (and validate) training on Corporate Values, one could reasonably infer that the program exists, but the details (standard) were inadequate; thus, this latent cause can be categorized as an “S – Inadequate Program Standards”.
Note the Latent Cause is stated in unique and specific terms relevant to the loss incident RCA.

## Slide 10
Example: Examine One Root in an RCA: Latent Cause & Recommendation
10
Chapter 4.5: Linking Latent Causes to Recommendations
Equipment found in defective state
Improper Risk Taking Improper Motivation
Basic Cause
Immediate Cause
Incident Description
Latent Cause
Inadequate Standard
Causes in the Root Cause Analysis
Category of Cause
Type of Cause
Sub-standard Work Practice
Mngmt System did not check that the IM understood Corporate Values: “Safety always before Production” as part of the communications plan.
IM had not yet learned (i.e. carunderstood) that safety checks must be done before Prod’n checks
IM prioritized Mtce work on Prod’n Equipment over Safety Equipment
Industrial Mechanic (IM) did not follow / implement procedure
LC-S: The management communications program did not include steps in the communications plan to check that new employees could explain Corporate Values. #1 MLCA
Recommendation!
A recommendation to address this latent cause:
Improve the “Corporate Values” Communications Plan:
  Confirm the organization has established corporate values
  Include steps in the communications plan to confirm that new employees can explain the Corporate Values.
  Implement a job observation audit system so management can confirm alignment to corporate values i.e. that the communications plan is effective.
Notes: 10
Note the Recommendation reflects the Latent Cause in its wording!

## Slide 11
Please confer (pen-to-paper, Zoom Chat Open)
What recommendations could you make for each latent cause?
  LC1-S: The leadership program did not include a standard to specify the roles and responsibilities for oversight to drive accountability for safe operation and maintenance of the tailings storage facility. RME#1 MLCA
  LC2-S: The risk assessment program did not include a standard to identify and assess hazards of the TSF foundation and hydraulic conditions while the TSF was in operation. #2 RA&MR
  LC3-S: The design program standard for applying the factors of safety during the design phase of the TSF project did not reference the necessary calculation guidelines from the Mining Association of Canada. #7 DC&SU
  LC4-C: The employee competency work process (standard) for recruiting, selecting, and hiring new employees was not followed. RME #9 EC&T
11
ALE #2: Mount Polley LI: Recommendations Based on LCs?
Chapter 4.5: Linking Latent Causes to Recommendations
Notes: 11

## Slide 12
Use the categories and sub-categories from the C&E Model to test and determine if you have “drilled sufficiently deep” i.e. check if you have drilled down to the latent cause, or still at a basic or intermediate cause.
As will be seen, the nature of the recommendation can also reveal if you are at a latent cause or still at a basic cause.
Test and Differentiate – Immediate, Basic, and Latent Causes:
12
Chapter 4.5: Linking Latent Causes to Recommendations
Basic Cause
Latent Cause
Weakness in Management System Element #.
Engineering Factors Job Factors Personal Factors
Basic Cause
Latent Cause
Inadequate Program Inadequate Standards Inadequate Compliance
Recommendation?
2
3
4b
4a
5
1
Notes: 12

## Slide 13
Example: Consider this RCA One-root Construct:
13
Chapter 4.5: Linking Latent Causes to Recommendations
Petroleum fire
Petrol released from pump casing
Pump casing corroded (failed)
Casing material was incompatible
Improper material was used
Pump design was incorrect
The refinery design program did not include a standard to design pumps for this process service
LOSS INCIDENT
Incident description
Intermediate / triggering event
IC: Sub-standard condition
intermediate
intermediate
BC: Design – inadequate tech. design
LC-S: RME#7 DC&SU
CATEGORIES
Notes: 13
This in-class active learning exercise is designed to prompt your thinking about the different causes and the different recommendations (actions) that one would undertake to address the loss incident. Recommendations can be made to address immediate causes, basic causes, and latent causes. In a root cause analysis, it is desired to discover the latent causes, and implement recommendations to address those latent causes. This is the only means to prevent the recurrence of the loss incident.
Recall from our discussion on RCA Tool and the C&E Model to categorise the types of causes. One last in-class exercise … think about the latent cause. What would your recommendation be?

## Slide 14
Example: What are some recommendations on the Causes?
14
Petroleum fire
Petrol released from pump casing
Pump casing corroded (failed)
Casing material was incompatible
Improper material was used
Pump design was incorrect
The refinery design program did not include a standard to design pumps for this process service
LOSS INCIDENT
RECOMMENDATIONS
Chapter 4.5: Linking Latent Causes to Recommendations
?
Notes: 14
Note the effectiveness of actions on each of the causes, and the effectiveness of preventing recurrence:
> “Replace the pump” does not prevent a recurrence.
> “Correct the design specification for this kind of pump” prevents recurrence in pumps of the same process service.
> “Correct the work process …” prevents recurrence in all pumps in all process services. This one addresses the latent cause.

## Slide 15
Example: Recommendations on the Causes
15
Petroleum fire
Petrol released from pump casing
Pump casing corroded (failed)
Casing material was incompatible
Improper material was used
Pump design was incorrect
The refinery design program did not include a standard to design pumps for any process service
LOSS INCIDENT
Replace the pump.
Correct the design specification for pumps in this kind of process service.
Create and implement a standard for writing specifications and designing pumps for all pumps in all services at this refinery.
RECOMMENDATIONS
Chapter 4.5: Linking Latent Causes to Recommendations
Notes: 15
Note the effectiveness of actions on each of the causes, and the effectiveness of preventing recurrence:
> “Replace the pump” does not prevent a recurrence.
> “Correct the design specification for this kind of pump” prevents recurrence in pumps of the same process service.
> “Correct the work process …” prevents recurrence in all pumps in all process services. This one addresses the latent cause.

## Slide 16
ALE #3: Most Effective Recommendation to Prevent Recurrence?
16
Chapter 4.5: Linking Latent Causes to Recommendations
Petroleum fire
Petrol released from pump casing
Pump casing corroded (failed)
Casing material was incompatible
Improper material was used
Pump design was incorrect
The refinery design program did not include a standard to design pumps for any process service
LOSS INCIDENT
RECOMMENDATIONS
Replace the pump.
Correct the design specification for pumps in this kind of process service.
Create and implement a standard for writing specifications and designing pumps for all pumps in all services at this refinery.
Which recommendation is most effective for preventing a recurrence of this incident? MM-Poll:
Notes: 16
Note the effectiveness of actions on each of the causes, and the effectiveness of preventing recurrence:
> “Replace the pump” does not prevent a recurrence.
> “Correct the design specification for this kind of pump” prevents recurrence in pumps of the same process service.
> “Correct the work process …” prevents recurrence in all pumps in all process services. This one addresses the latent cause.

## Slide 17
Note the Effectiveness of Actions on Causes to Prevent Recurrence:
17
Petroleum fire
Petrol released from pump casing
Pump casing corroded (failed)
Casing material was incompatible
Improper material was used
Pump design was incorrect
The refinery design program did not include a standard to design pumps for any process service
LOSS INCIDENT
Replace the pump. Note: This actions fixes the pump that failed, but not any other pumps in the refinery, now or in the future.
Correct the design specification for pumps in this kind of process service.
Note: This action fixes the design for all pumps in this service, now and in the future, but not any pumps in other services.
Create and implement a standard for writing specifications and designing pumps for all pumps in all services at this refinery.
Note: This fixes all designs for all pumps in all services.
RECOMMENDATIONS
NO PREVENTION
PREVENTS ONLY SAME SERVICE
Chapter 4.5: Linking Latent Causes to Recommendations
MOST EFFECTIVE!PREVENTS DESIGN ERRORS ON ALL PROCESS SERVICES
Notes: 17
Note the effectiveness of actions on each of the causes, and the effectiveness of preventing recurrence:
> “Replace the pump” does not prevent a recurrence.
> “Correct the design specification for this kind of pump” prevents recurrence in pumps of the same process service.
> “Correct the work process …” prevents recurrence in all pumps in all process services. This one addresses the latent cause.

## Slide 18
What does a good “recommendation for action” statement look like?
The previous slides give you a good idea about differentiating an action to address an immediate cause, a basic cause, and a latent cause; however, this latent cause statement is not the best model. So, let’s consider these two latent cause statements in two different roots:
The auditing program did not include a standard to define how and when to perform regular / periodic internal and external evaluations for on-going construction practices.
The auditing program did not include a standard to define how and when to perform regular / periodic internal and external evaluations for inspection documents and the review of those documents.
Thus, your action for each recommendation should then address exactly what is missing or what needs to be addressed in order to close the gap:
Implement a standard for the auditing program to define how and when to perform regular / periodic internal and external evaluations for on-going construction practices.
Implement a standard for the auditing program to define how and when to perform regular / periodic internal and external evaluations for inspection of on-going construction documents and the review of those documents.
Recommendation for Action:
18
Chapter 4.5: Linking Latent Causes to Recommendations
Notes: 18

## Slide 19
What does a good “recommendation for action” statement look like?
Alternatively, one could create a combined recommendation to address both latent causes:
Implement an auditing program that ensures regular internal and external evaluations are performed for ongoing construction practices, as well as for inspection documents and the review of those documents.
BUT the phrase "Implement an auditing program to ensure inspections are done" is somewhat weak i.e. it is not expressed in concrete terms.
The combined recommendation can be expressed as either:
Implement an auditing program standard to define how and when to perform regular / periodic internal and external evaluations for ongoing construction practices, as well as for inspection documents and the review of those documents.
Implement a standard within the auditing program to define how and when to perform regular / periodic internal and external evaluations of on-going construction practices, and the as well as for inspection documents and the review of those documents.
Recommendation for Action:
19
Chapter 4.5: Linking Latent Causes to Recommendations
Notes: 19

## Slide 20
Each root ends in one unique latent cause, and one latent cause can align to only one risk management system element.
The latent cause is stated in terms relevant to one unique management system element.
A recommendation for action should readily follow from a well-stated latent cause. It should be in concrete terms.
A recommendation that addresses a latent cause is MOST effective in preventing a recurrence of a loss incident through the identified root in the RCA.
Summary & Key Lessons:
20
Chapter 4.5: Linking Latent Causes to Recommendations
Notes: 20

## Slide 21
Any questions?
Notes: 21

## Slide 22
RCA of an LI: Match the Categories Assignment #2 Question #1:
22
Chapter 4.5: Linking Latent Causes to Recommendations
Petroleum fire
Petrol released from pump casing
Pump casing corroded (failed)
Casing material was incompatible
Improper material was used
Pump design was incorrect
The refinery design program did not include a standard to design pumps for this process service
LOSS INCIDENT
Incident description (abbreviated)
Second intermediate
IC: Sub-standard condition
Third intermediate
First intermediate
BC: Design – inadequate tech. design
LC-S: RME#7 DC&SU
CATEGORIES
Notes: 22
This in-class active learning exercise is designed to prompt your thinking about the different causes and the different recommendations (actions) that one would undertake to address the loss incident. Recommendations can be made to address immediate causes, basic causes, and latent causes. In a root cause analysis, it is desired to discover the latent causes, and implement recommendations to address those latent causes. This is the only means to prevent the recurrence of the loss incident.
Recall from our discussion on RCA Tool and the C&E Model to categorise the types of causes. One last in-class exercise … think about the latent cause. What would your recommendation be?